## Slide 1
HW1 · HDD PERFORMANCE TEST
Storage I/O
Performance Test
Block Writes | Sequential Reads | Random Reads
HDD results are the focus. SSD data appears on one comparison slide.
Notes: This report focuses on the HDD results in homework1_hdd_result/run. The final slide compares them with the earlier SSD run. Sources: both sets of experiment CSV files and homework1.pdf. No name or student ID was provided, so none is shown.

## Slide 2
HDD · EXPERIMENT DESIGN
Test Data and Measurement Method
Data written per phase
256 KiB
Repeating byte pattern: 1–255
Write block sizes
18
From 1 B to 128 KiB
Runs per block size
256×
Mean time across runs
READ TEST
File 19: 256 MiB · Sequential: one full pass · Random: 1,024 × 256 KiB
Timing excludes open() and close(). Experiment 2 measured each read method once.
Notes: Sources: homework1.pdf, experiment2.c, and the experiment1_results.csv and experiment2_results.csv files for both runs. Each HDD block size has 256 measurements; charts use arithmetic means. Experiment 2 has one measurement per read method.

## Slide 3
EXPERIMENT 1 · HDD · 18 BLOCK SIZES · 256 RUNS EACH
Mean write time drops sharply as blocks get larger
Chart: Block size (bytes; K = KiB; powers of 2)
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | 1K | 2K | 4K | 8K | 16K | 32K | 64K | 128K
Mean write time | 1092.1794 | 552.9115 | 275.9011 | 139.0572 | 70.5092 | 36.9868 | 17.8127 | 9.3028 | 5.0387 | 2.8923 | 1.8717 | 1.325 | 0.9689 | 1.0227 | 1.0604 | 1.0506 | 1.0739 | 1.1144
1 B: 1092.2 ms | 4 KiB: 0.969 ms | 128 KiB: 1.114 ms
Notes: Source: homework1_hdd_result/run/experiment1_results.csv. Each of the 18 block sizes has 256 measurements. The x-axis uses powers-of-two categories, spaced evenly to represent log2 block size; the y-axis is linear in milliseconds. Small blocks take much longer, making differences above 4 KiB hard to see here. The next slide zooms in on that range.

## Slide 4
EXPERIMENT 1 · ZOOMED VIEW · HDD MEANS
Write time stays near 1 ms beyond 4 KiB
Chart: 區塊大小
| 4 KiB | 8 KiB | 16 KiB | 32 KiB | 64 KiB | 128 KiB
Mean write time | 0.9689 | 1.0227 | 1.0604 | 1.0506 | 1.0739 | 1.1144
Lowest mean: 4 KiB = 0.969 ms | 128 KiB = 1.114 ms
Notes: Source: homework1_hdd_result/run/experiment1_results.csv. The y-axis is zoomed to 0.8–1.2 ms to show small differences among larger blocks. The 4 KiB mean is the lowest; the mean rises slightly by 128 KiB. The improvement levels off rather than continuing to fall.

## Slide 5
ANALYSIS · FIXED WRITE SIZE: 256 KiB
Larger blocks require fewer write() calls
1 B BLOCK
262,144
write() calls
One call per byte
4 KiB BLOCK
64
write() calls
4,096× fewer calls
128 KiB BLOCK
2
write() calls
Lowest call and loop overhead
Fewer calls reduce the cumulative cost of kernel transitions, function calls, and loop management.
Beyond about 4 KiB, I/O and file-system overhead account for more of the time, so larger blocks add little benefit.
Notes: Calculation: 262,144 bytes per phase divided by block size. A 1-byte block corresponds to 262,144 calls; 4 KiB corresponds to 64; 128 KiB corresponds to 2. The write loop handles short writes, so a very small number of runs could make more system calls. This slide explains why larger blocks are generally faster, as required by homework1.pdf.

## Slide 6
EXPERIMENT 2 · 256 MiB READ IN BOTH TESTS
Random reads took longer in this HDD run
Chart: Read method
| Sequential | Random
HDD read time | 51.5349 | 57.9681
Sequential: 51.53 ms | Random: 57.97 ms | Random was 12.5% slower
One run per method; sequential ran first. Cache and test order may affect results.
Notes: "Experiment 2 compares the two reading patterns. Both tests move the same amount of data — 256 megabytes. Sequential reading finishes in 51.5 milliseconds. Random reading — 1,024 reads of 256 KB scattered with lseek() — takes 58.0 milliseconds. So random reading is about 12.5 percent slower."

## Slide 7
EXPERIMENT 2 · INTERPRETATION
Sequential and Random Access
Sequential Reads
Data is read from nearby locations, supporting sustained transfer. The operating system may also prefetch upcoming data.
Random Reads
Requests jump between locations. If data must come from the platters, head seeks can add latency.
In this HDD run, random reads took 57.97 ms, 12.5% longer than the 51.53 ms sequential read. Sequential ran first and each method was measured once. File caching may have reduced or changed the gap. Alternate test order and repeat the measurements for a more reliable comparison.
Design implication: reduce random I/O, combine small requests, or choose storage suited to the access pattern.
Notes: "Why is random slower? Two reasons. First, sequential access lets the kernel's read-ahead work: it predicts the next blocks and fetches them before we ask. Random jumps break that prediction every time. Second, each random read requires an extra lseek() to reposition the file offset, adding syscall and bookkeeping cost.
But here's an important observation for our conclusions: 5,209 megabytes per second is far faster than any hard drive — so the data was clearly being served from the page cache, because we had just written that file. The 12.5% gap mostly reflects seek and syscall overhead, not physical disk movement. On a cold hard disk, random access would be dramatically worse — seek times measured in milliseconds instead of nanoseconds. This is exactly why cache state must always be stated in storage benchmarks."

## Slide 8
HDD RESULTS · SUMMARY
What have we learned?
01
Larger blocks reduce calls
02
Read method matters
03
System calls should be minimized
Notes: "So, what should a practitioner take away?
One: choose block sizes of at least 4 KB — ideally the page size. Smaller blocks waste CPU on syscalls; larger blocks add nothing.
Two: sequential access is cheaper than random, so design systems around streaming and appending, and batch small writes into buffers.
Three: throughput rises from 0.24 MB/s at 1-byte blocks to about 270 MB/s at 4 KB — a direct result of making fewer, better-amortized system calls.
And four: the gains saturate. Beyond the page size, you're limited by the data path, not the API — bigger is not always better."